## Slide 1: ALGORITHM TO PERFORM FLUSH Air DATA SENSING (FADS)

## Slide 2: OVERVIEW
INTRODUCTION
PROBLEM STATEMENT (OBJECTIVE )
ALGORITHM
APPLICATION OF ALGORITHM – (ON ABSTRACT PRESSURE DATA OBTAINED FROM SIMULATION OF 2D AEROFOIL).
RESULTS AND CONCLUSION

## Slide 3: INTRODUCTION
Flush air data sensing system (FADS) forms admission-critical subsystem in re-entry vehicles. It makes use of surface pressure measurements from the nose cap of the vehicle for deriving air data parameters such as angle of attack, angle of sideslip, Mach number, etc. of the vehicle. These parameters are used by the flight control and guidance systems, and also assist in the overall mission management. The Space Shuttle has used a nonlinear regression based algorithm for this. ‘Triples’-based algorithm was proposed for the X-33 vehicle. Neural network-based systems were also developed for FADS.
Static Pressure measured by pressure ports .
Aerodynamic models –Approximate equations used to estimate data
Calibration-
Using correction data sets
Air data sets
Fig. FADS Installation at nose of F-18 aircraft.

## Slide 4: OBJECTIVES
MAIN OBJECTIVE
To come up with an algorithm which involves search and interpolation approaches to find out the aerodynamic parameters like angle of attack(α), Mach-number (M), Side-slip angle(β) & Altitude (h) corresponding to the pressure measured by Transducers .Algorithm eliminates the dependency on Aerodynamic models for data interpretation.
To find suitable location for Pressure Transducers on Aircraft’s body such that measurement is not affected by the disturbing flow field around the aircraft.
CURRENT OBJECTIVE
To develop an algorithm and apply it to find the aerodynamic parameter α & M corresponding to the pressures on five locations present on the 2D aerofoil and validate it with results of simulation performed in HI-FUN 3D.

## Slide 5: ALGORITHM
Structural Arrangement of Dataset (pressure)
Search Operation to find input data location.
Bilinear Interpolation operation.
Output
Aerodynamic parameter
Fig. Algorithm Flow Chart
1. Arranging Pressure data obtained from experiments or Simulations at different aerodynamic condition.
2. Searching common location for given input pressure values.
3. After finding common location performing Bilinear Interpolation.
4. After Bilinear interpolation Aerodynamic Parameters are obtained .

## Slide 6: APPLICATION OF ALGORITHM
Euler Simulation on 2D Aerofoil (NACA 0012) is performed and pressure values at different M and α is used to check the algorithm and to find the error.
Port1 (P1)
Port2 (P2)
Port3 (P3)
Port4 (P4)
Port5 (P5)
Positions of location selected for ports
Port1 – Leading edge .
Port2 & port3 – 20% of chord length.
Port4 & Port 5- 50% of chord length.
Fig . NACA 0012 Aerofoil

## Slide 7
Plots of Cp values on M – α carpet.

## Slide 8
Arrangement of Dataset (Pressure Data).
32 | 31 | 30 | 29
25 | 26 | 27 | 28
24 | 23 | 22 | 21
17 | 18 | 19 | 20
16 | 15 | 14 | 13
9 | 10 | 11 | 12
8 | 7 | 6 | 5
1 | 2 | 3 | 4
0.2 0.3 0.4 0.5 0.6
12
10
8
6
4
2
0
-2
-4
Angle of attack (α)
Mach number (M)
(Box.no)1
At each node Pressure at all five ports P1 to P5 is stored for corresponding M and α combinations. As P(M, α).
At this node
P1(0.2 ,-4) ……to p5(0.2,-4)

## Slide 9
2. Search Operation (for a given input data set)
32 | 31 | 30 | 29
25 | 26 | 27 | 28
24 | 23 | 22 | 21
17 | 18 | 19 | 20
16 | 15 | 14 | 13
9 | 10 | 11 | 12
8 | 7 | 6 | 5
1 | 2 | 3 | 4
12
10
8
6
4
2
0
-2
-4
0.2 0.3 0.4 0.5 0.6
Angle of attack (α)
Mach number (M)
Let,
P ibmax = Maximum Pressure of a box.
P ibmin = Minimum Pressure of a box.
Pi = Input Pressure (where i represent port number, i.e. i=1 to 5)
Pimin = Minimum Pressure value of a Port
Pimax = Minimum Pressure value of a Port
ΔPi = Resolution of a slot ,
ΔPi = (Pimax - Pimin)/ N
N = number of slots
To make search easier two dimensional boxes are related to one dimensional slots .
2D- BOXES
1 | 2 | 3 | . | . | . | . | . | . | N
Pimin
Pimax
ΔPi
1D -SLOTS

## Slide 10
Relating 2D Box to 1D slot
Box 1
P ibmax
P ibmin
1 | 2 | Smin | . | . | . | . | Smax | . | N
Pimin
Pimax
ΔPi
We will find the slots in which the box lies by using :
Smin= (P ibmin- Pimin)/ ΔPi (lower limit of slot number )
Smax= (P ibmax- Pimin)/ ΔPi (upper limit of slot number )
Box will lie from slot Smin to Smax
Example
Finding out slot range for port i=4 , and box =1 where we have , P 4bmin= 100269.48 , P 4bmax=101095.9
P4min= 88345.06847 & ΔP4= 398.4625290625
Smin= (100269.48- 88345.06847)/ 398.4625290625= 29.92605492430035≈30
Smax= (101095.9-88345.06847)/ 398.4625290625= 32
So for pressure 4 Box 1 lies from slot 30 to 32.

## Slide 11
Finding Box numbers lying in a slot when a Pressure Input is Given
Angle of attack (α)
32 | 31 | 30 | 29
25 | 26 | 27 | 28
24 | 23 | 22 | 21
17 | 18 | 19 | 20
16 | 15 | 14 | 13
9 | 10 | 11 | 12
8 | 7 | 6 | 5
1 | 2 | 3 | 4
12
10
8
6
4
2
0
-2
-4
Mach number (M)
0.2 0.3 0.4 0.5 0.6
1 | 2 | 3 | Sn | . | . | . | . | . | N
Pimin
Pimax
ΔPi
If Pressure Pi is given then
Sn= (Pi- Pimin)/ ΔPi slot number which contains Pi
Then there will be boxes In slot where Pressure Pi will lie
Example
If P4=100900, P4min= 88345.06847 & ΔP4= 398.4625290625 then
Sn= (100900- 88345.06847)/ 398.4625290625
= 31.50843709078281 ≈ 32
So now boxes in which P4 will lie will be in slot 32 i.e Box1

## Slide 12: Example to find a common box for 5 pressure values
32 | 31 | 30 | 29
25 | 26 | 27 | 28
24 | 23 | 22 | 21
17 | 18 | 19 | 20
16 | 15 | 14 | 13
9 | 10 | 11 | 12
8 | 7 | 6 | 5
1 | 2 | 3 | 4
12
10
8
6
4
2
0
-2
-4
0.2 0.3 0.4 0.5 0.6
Angle of attack (α)
Mach number (M)
1 | 2 | 3 | Sn | . | . | . | . | . | N
1 | 2 | 3 | Sn | . | . | . | . | . | N
1 | 2 | 3 | Sn | . | . | . | . | . | N
1 | 2 | 3 | Sn | . | . | . | . | . | N
1 | 2 | 3 | Sn | . | . | . | . | . | N
P1
P2
P3
P4
P5
Pressure | Boxes
P1 =101005.992654 | 1,2,15,16,18,19,20,21
P2 =86124.4920577 | 17,24,25,32,15,18,11,14,12
P3 =107892.930975 | 15,18,23,26,31,14,12,13
P4 =97540.108370 | 24,25,32,10,15,18,23,6,11,4,5
P5 =101108.04109 | 14,24,18,19,20,21
Common box= 18

## Slide 13: 3.Applying Bilinear Interpolation
Formula derived from Bilinear Interpolation to calculate Mach-Number (M) and angle of attack (α) for two pressure input, which are supposed to be obtained at same M & α
Pi =
To solve for Mach number (m) and Angle of Attack (a) we need two equations which can be obtained by choosing any of two pressure values from P1 to P5 .
[ (α2-a){(M2-m) Pi1+(m-M1)Pi2}+(a-α1){(M2-m)Pi4+(m-M1)Pi3]
(α2- α1)( M2- M1)
Common Box
1
4
3
2
(M1 α1)
Pi1
(M2 α1)
Pi2
(M2 α2)
Pi3
(M1 α2)
Pi4
(m a)
Pi

## Slide 14
Example for Application of Bilinear Interpolation to solve for Mach number(m) and angle of Attack(a)
Since we have five Pressure values it will lead to (five equations to solve for two variable) Overdetermined system of equations so we will take each possible pair of Pressures and average the result for m and a .
For pressure values :
P1 =101005.992654
P2 =86124.4920577
P3 =107892.930975
P4 =97540.108370
P5 =101108.04109
common box =18 ,
After Averaging all the m and a
m=0.325
a= 4.5
Common box=18
1
2
3
4
(0.3 4)
(0.4 4)
(0.4 6)
(0.3 6)

## Slide 15: Mach number and angle of attack used for Simulation:
Random Pair of Mach Number (M) and Angle of attack (α) are generated using Matlab so that the whole domain gets covered .
12
10
8
6
4
2
0
-2
-4
0.2 0.3 0.4 0.5 0.6
Angle of attack (α)
Mach number (M)
S.N | Mach (M) | AOA (α)
1 | 0.3494 | -3.6536
2 | 0.235 | 10.5691
3 | 0.456 | 8.8089
4 | 0.2722 | 7.9336
5 | 0.4893 | 2.1329
6 | 0.339 | 5.8765
7 | 0.3535 | 4.4808
8 | 0.4893 | -3.5201
9 | 0.4642 | -0.3566
10 | 0.2895 | 0.4011
1
2
3
4
5
7
6
8
9
10

## Slide 16: RESULT AND CONCLUSION
S.N | Exact (Given for Simulation) |  | Estimated (From Algorithm) |  | ΔM=(M-m) | Δα= (α-a) | %error M= (ΔM/M)*100 | %error α = (Δα/α)*100
 | Mach (M) | AOA(α) | Mach (m) | AOA(a) |  |  |  | 
1 | 0.3494 | -3.6536 | 0.347568 | -3.5789 | 0.005243 | 0.020445 | 0.524274 | 2.044523
2 | 0.235 | 10.5691 | 0.235303 | 10.21631 | -0.00129 | 0.033379 | 0.12888 | 3.337926
3 | 0.456 | 8.8089 | 0.469022 | 8.6573 | -0.02856 | 0.01721 | 2.8558 | 1.720985
4 | 0.2722 | 7.9336 | 0.276326 | 7.622691 | -0.01516 | 0.039189 | 1.51578 | 3.918887
5 | 0.4893 | 2.1329 | 0.484457 | 2.176458 | 0.009898 | -0.02042 | 0.989792 | 2.0422
6 | 0.339 | 5.8765 | 0.33874 | 5.653321 | 0.000766 | 0.037978 | 0.076594 | 3.797825
7 | 0.3535 | 4.4808 | 0.349711 | 4.490431 | 0.010718 | -0.00215 | 1.071822 | 0.21494
8 | 0.4893 | -3.5201 | 0.487708 | -3.46066 | 0.003253 | 0.016886 | 0.325281 | 1.688626
Table . Error and Error percentage between exact and estimated M and α

## Slide 17
Plot of Exact and Estimated Mach Number & Angle of Attack
Chart: M vs α
| 0.33900000000000002 | 0.45600000000000002 | 0.2722 | 0.28949999999999998 | 0.34939999999999999 | 0.35349999999999998 | 0.4642 | 0.48930000000000001
Exact | 5.8765 | 8.8089 | 7.9336 | 0.4011 | -3.6536 | 4.4808 | -0.3536 | 2.1329
Estimated | 5.7582 | 9.4957 | 7.8626 | 0.3871 | -3.5789 | 4.4258 | -0.4351 | 2.1181

## Slide 18
Mach Number is estimated with maximum error of 2.85 % while Angle of attack with maximum error of 3.918887 % .
Probable Reasons Behind Error
Bilinear Interpolation (limitation in degree).
Averaging of the estimated Mach (m) and AOA (α) .
Coarseness in resolution of boxes .
Fields of Improvement
Efficiency of Code .
Better Interpolation Technique (Polynomial interpolation).
Improvement in Search technique.

## Slide 19: THANK YOU